## Slide 1: Water Emissions

## Slide 2: Outline
1. Learning objectives
2. Review of basics (5m)
3. Level 1 What? Why? (Compilers)
  Concepts (15m)
  Group exercise & Discussion (30m)
4. Level 2 (Data providers)
  Data options, examples & issues (15m)
  Group exercise & Discussion (15m)
5. Closing Discussion (10m)
Manila
Outline
Notes: This will be a combination presentation, group exercise and discussion. The entire process will take about 90 minutes.
Before we start, I’d like to emphasize that I recognize that some of you will be more expert than I in some of the topics we will discuss.
One objective, is to bring everyone to the same level of understanding of this topic. This requires a simplification of the principles and concepts.
The training unit is still being developed and I look forward to your input to improve it.

## Slide 3: Learning objectives: Levels 1 and 2
  Level 1:
    Understand why Emissions to Water are important and how they link to policy
    Understand the basic concepts of Accounting for Emissions to Water
    Understand how water is treated in the SEEA
    Learn the steps of compiling a Water Emissions Account
  Level 2:
    Understand the data options and sources
    Understand the important conceptual issues
    Be aware of how other countries have approached Water Emissions Accounting
Learning Objectives
Notes: Please ask questions and comment during the presentation (as long as you keep it high level = clarification, correction)

## Slide 4: Are we polluting our water assets?
Water Assets
Abstraction & Use
Returns
Renewable supply
The economy
2. Review of basics
Emissions

## Slide 5: Are we polluting our water assets?
Water Assets (stock)
Renewable supply
Abstraction and use
Returns
2. Review of basics

## Slide 6: Water emissions accounting
What?
  Effluent: quantity of wastewater in m3 (regardless of quality)
  Emission: quantity of substance in the effluent (in tonnes)
Why?
  Policies on water quality & security, resources management
  Links to economic accounts (EPE, intensities)
  Basis for SEEA-WATER, SEEA-EEA (ecosystems), FDES 3.2
  Indicators:
    Total water emissions supply (who makes it?)
    Total water emissions (who treats it?)
    Water emissions intensity/productivity (who makes the most?)
    Treatment capacity (is there enough?)
2. Review of basics

## Slide 7: Waste water in the news
2. Review of basics

## Slide 8: What is the problem?
We put things into the water stream:
  Pathogens, poisons, metals: Make us & ecosystems sick
  Organic materials: Cause eutrophication (too little oxygen)
  Heat: Changes in ecosystems
  Emerging issue: microbeads, microplastics (effect not certain)
Untreated wastewater returns to
  Water supply (need to treat it again)
  Environment (soil, runoff to rivers, groundwater, ocean)
Emissions to water is
  a waste that can be captured & reused
2. Review of basics

## Slide 9: Water Emissions Account
Learning objectives
Review of Level 0 (5m)
Level 1 (Compilers)
  Concepts (15m)
  Group exercise & Discussion (30m)
Level 2 (Data providers)
  Data options, examples & issues (15m)
  Group exercise & Discussion (15m)
Closing Discussion (10m)
3. Level 1

## Slide 10: In simple terms…
Generation
  What, how much and by whom?
Collection, treatment and reuse
  Waste Water Treatment Plants (WWTP)
    Reuse of water (usually cleaner)
    Reuse pollutants removed
Discharge to environment
Source: UNSD 2014
3. Level 1
Releases in wastewater
106
Pollutants in water for reuse
4
Pollutants removed by WWTPs
6
Waterborne emissions to the environment
34

## Slide 11: In simple terms…
Generation
  What, how much and by whom?
Collection, treatment and reuse
  Waste Water Treatment Plants (WWTP)
    Reuse of water (usually cleaner)
    Reuse pollutants removed
Discharge to environment
Source: UNSD 2014
3. Level 1

## Slide 12: Water emissions in the water cycle
Source: WWAP
3. Level 1
Water emissions flows

## Slide 13: Measuring it: red lines are wastewater!
Source: UNSD 2014
3. Level 1
Notes: The water PSUT don’t say what’s in it.

## Slide 14: What does a Water Emissions Account look like?
Start with gross volumes of water released (m3):
To establish flows to environment or to treatment
SEEA Water Supply/Use provides estimates of volumes of water treated and discharged
Include…
Point sources: sewerage facilities, power plants, industry
Non-point sources: urban runoff, agriculture
Estimate quantities of substances
From concentrations
From “factors” (e.g., per household per day, per m3 effluent)
3. Level 1
Select relevant substances (tonnes)
BOD (organic substances)
COD (inorganic substances)
Suspended solids
Phosphorous (nutrient)
Nitrogen (nutrient)
Solid wastes dumped into water are in Solid Waste Account
For each, account for…
Supply
Gross releases of substances (tonnes):
Release to other economic units
Use
Emissions received by the environment
Collection by other economic units
Notes: BOD: Biological Oxygen Demand (organic substances)
COD: Chemical Oxygen Demand (inorganic substances)
Suspended Solids (things you can see) (a.k.a. TSS)
Phosphorous (nutrient) (a.k.a. TP)
Nitrogen (nutrient) (a.k.a. TN, or TKN)

## Slide 15: What does a Water Emissions Account look like?
Start with gross volumes of water released (m3):
  To establish flows to environment or to treatment
  SEEA Water Supply/Use provides estimates of volumes of water treated and discharged
Include
  Point sources: sewerage facilities, power plants, industry
  Non-point sources: urban runoff, agriculture
Estimate quantities of substances
  From concentrations
  From “factors” (e.g., per household per day, per m3 effluent)
3. Level 1

## Slide 16: What does a Water Emissions Account look like?
Select relevant substances (tonnes)
  BOD: Biological Oxygen Demand (organic substances)
  COD: Chemical Oxygen Demand (inorganic substances)
  Suspended Solids (things you can see) (a.k.a. TSS)
  Phosphorous (nutrient) (a.k.a. TP)
  Nitrogen (nutrient) (a.k.a. TN, or TKN)
  Note: Solid wastes dumped into water are in Solid Waste Account
For each, account for
  Supply:
    Gross releases of substances (tonnes):
    Releases to other economic units
  Use:
    Emissions received by the environment
    Collection by other economic units
3. Level 1

## Slide 17: Flows in water emissions accounts
3. Level 1
Environment
(e.g., surface water, oceans and seas)
Industry
(e.g., mining, manufacturing)
Sewage industry
Households

## Slide 18: The supply-use chain (kind of)
Supply (tonnes) | Generation |  |  | From environment | Total
 | Sewage industry | Other industries | Households |  | 
Emission of substances by type |  |  |  |  | 
Releases to other economic units |  |  |  |  | 
Use (tonnes) | Generation |  |  | To environment | Total
 | Sewage industry | Other industries | Households |  | 
Emission received by the environment |  |  |  |  | 
Collection by other economic units |  |  |  |  | 
Direct releases
To sewage
Release after treatment
3. Level 1

## Slide 19: What does a water emissions Account look like?
Physical supply
Emissions are direct discharge to the environment
Releases to other economic units are amounts sent for treatment
2,712 + 8,950 = 11,662
2,712/11,662 = 23%
3. Level 1
How much BOD/COD do households generate?
What % is untreated?
What industry is generating all this?
Agriculture
Notes: This is simpler than water, energy and physical supply/use for natural inputs.

## Slide 20: What does a water emissions Account look like?
Physical use
Emissions received are total discharge to the environment
Collection by other economic units are amounts sent for treatment
3. Level 1
If the sewerage industry
Collects 16,877T BOD/COD,
Emits 5,994T (previous slide)
Where does the rest
(10,893T) go?
Solid waste or sludge pond
Notes: Answer: Solid waste or sludge pond
???: presume returns to water supply from water PSUT? Emissions removed = solid waste

## Slide 21: Examples of Water emissions-related SDG indicators
6.2.1 Proportion of population using safely managed sanitation services
6.3.1: Percentage of wastewater safely treated
6.3.2 Proportion of water bodies with good ambient quality
6.4.2 Level of water stress: freshwater withdrawal as a proportion of available freshwater resources
3. Level 1
Notes: https://ec.europa.eu/eurostat/statistics-explained/index.php/SDG_6_-_Clean_water_and_sanitation_(statistical_annex) : This one has data by year and country
https://unstats.un.org/unsd/envstats/fdes/SDGsInd_BasicSetMatrix.pdf : This one has statistics used in the SDG Indicator corresponding to BSES (SDG indicator can be compiled either fully or partially from BSES statistics)

## Slide 22: Compilation Group Exercise (30m)
Situation:
  Have some source factors and gross discharge amounts
Objective (Groups of 3-5):
  Compile a Water Emissions Account
  Report results
3. Level 1
Notes: For the compilation exercise, we will
Take a simple Stock and Flow diagram and create a Water Asset Account.
Create a Supply and Use Table from a Supply and Use Diagram

## Slide 23: The situation
The country has a population of 50 million
85% are connected to the sewer network
A survey estimates that each person generates:
  60g of BOD/day
  130g of COD/day
  70g of Suspended Solids/day
Per year, agriculture applies 5MT of phosphorous and 10MT of nitrogen. All is emitted to the environment.
Industry discharges 5Mm3 of water per year. Tests show that, after own treatment, the average concentration of:
  Heavy metals is 3.2g/m3
  COD is 2.5kg/m3
The sewage industry is 80% efficient in removing BOD, COD and Suspended Solids
Compile the water emissions supply and use tables below.
What are the totals discharged to the environment?
3. Level 1

## Slide 24: The answers
Water Emissions Account
Per day, 50 million people generate
  60g BOD
  130g COD
  70G TSS
85% is treated
50,000,000 * .06 * 365/1000 *.85
15% is released to the environment
50,000,000 * .06 * 365/1000 *.15
3. Level 1

## Slide 25: The answers
Water Emissions Account
Agriculture applies 5MT Phosphorous and 10MT Nitrogen
Industry discharges 5Mm3 wastewater
COD is 2.5kg/m3
5,000,000 * 2.5/1000
Heavy metals are 3.2g/m3
5,000,000 * .0032/1000
Totals emitted to environment
3. Level 1

## Slide 26: The answers
Water Emissions Account
Per day, 50 million people generate
  60g BOD
  130g COD
  70G TSS
85% is treated
50,000,000 * .06 * 365/1000 *.85
15% is released to the environment
50,000,000 * .06 * 365/1000 *.15
3. Level 1

## Slide 27: The answers
Water Emissions Account
Agriculture applies 5MT Phosphorous and 10MT Nitrogen
Industry discharges 5Mm3 wastewater
COD is 2.5kg/m3
5,000,000 * 2.5/1000
Heavy metals are 3.2g/m3
5,000,000 * .0032/1000
Totals emitted to environment
3. Level 1

## Slide 28: Water Account
4. Level 2
Learning objectives
Review of Level 0 (5m)
Level 1 (Compilers)
  Concepts (15m)
  Group exercise & Discussion (30m)
Level 2 (Data providers)
  Data options, examples & issues (15m)
  Group exercise & Discussion (15m)
Closing Discussion (10m)

## Slide 29: Types of water emissions and sources
Group | Pollutant
Pathogens | Viruses, bacteria, helmiths
Organic matter | Bio-degradable
Nutrients | Nitrogen
 | Phosphorous
Poisonous substances | Metals
 | Persistent Organic Pollutants (POPs), PCBs, PBTs, etc.
Other | Heat
 | Colour
 | Microbeads/plastics
4. Level 2
*You can find main sources of the pollutants in Annex

## Slide 30: Good news! You don’t need to measure (much)
Data:
  Household emissions estimated from factors
    e.g., One household discharges 60g/day BOD
  Agriculture discharges all pesticides and fertilizers applied
  Industries are often regulated to limit emissions (standard)
    e.g., Plant xxx averages 100m3 effluent per day, BOD is 2.5kg/m3
  Industries may need to report on quantities released
    e.g., via Pollutant Release and Transfer Registry (PRTR)
Expertise:
  Statisticians
  Industrial engineers (to estimate discharge)
  Water supply and treatment specialists
4. Level 2
Notes: Discussion? E.g., what are the priorities, opportunities and constraints in your country to compiling Water Accounts?

## Slide 31: Common problems in compilation
Scope
Sewage treatment only covers amounts collected
(not generated)
Data Quality
Getting data from industries and farms with own treatment
Local emission factors
(urban/rural, high/low income, industry by type…)
Administrative data
Expenditures on fuel (by type), consumption of fuel
Energy utilities
Seasonality
Annual averages may hide seasonal variation and extremes
(e.g., seasonal operators, rainy/dry seasons)
Scale of data
National level data may hide regional variation
4. Level 2
Notes:   Scale of data (national level data may hide regional variation)
  Seasonality: Annual averages may hide seasonal variation and extremes (e.g., seasonal operators, rainy/dry seasons)

## Slide 32: Common problems in compilation
  Scope
    Sewage treatment only covers amounts collected (not generated)
  Data quality
    Getting data from industries and farms with own treatment
    Local emission factors (urban/rural, high/low income, industry by type…)
  Scale of data (national level data may hide regional variation)
  Seasonality: Annual averages may hide seasonal variation and extremes (e.g., seasonal operators, rainy/dry seasons)
4. Level 2
Notes: These are only a few of the challenges. Still, it’s not difficult to get started to assemble water accounts.

## Slide 33: Data options
Global data sources
  Agricultural fertilizers and pesticides: FAOStat (http://www.fao.org/faostat/en/#data)
  Wastewater (produced, collected, treated, capacity, untreated, use: FAO AquaStat (http://www.fao.org/nr/water/aquastat/data/query/index.html?lang=en)
    Very few data points for the Philippines
4. Level 2
Notes: Not much for the Philippines.

## Slide 34: PRTR: Pollutant Release and Transfer Registers
If your country have PRTR, USE IT!!
OECD: International guidelines & data clearinghouse
Usually large emitters of large quantities
Canada: National Pollutant Release Inventory (NPRI)
  Collected via mandatory questionnaire
  Only specific substances
  Publicly accessible  maps, data
  But…some substances, small emitters, mobile sources not covered
Source: https://www.ec.gc.ca/inrp-npri/
4. Level 2

## Slide 35: PRTR: Pollutant Release and Transfer Registers
OECD: International guidelines & data clearinghouse (PRTR)
Usually large emitters of large quantities
Canada: National Pollutant Release Inventory (NPRI)
  Collected via mandatory questionnaire
  Only specific substances
  Publicly accessible  maps, data
  But…some substances, small emitters, mobile sources not covered
Source: https://www.ec.gc.ca/inrp-npri/
4. Level 2

## Slide 36: Some Country examples
Canada:
  Using 3 different sources…
  No compilation of water emission accounts (report wastewater)
4. Level 2
Drinking Water Plants Survey (DKWP)
Volumes treated, quality of intake, outflow, costs
National Pollutant Release Inventory (NPRI)
Mandatory reporting of large amounts by large companies (by location)
Survey of Industrial Processes (SIP) (pilot)
Processes in place to limit pollutants (adjunct to NPRI)

## Slide 37: Some Country examples
Canada:
  National Pollutant Release Inventory (NPRI): mandatory reporting of large amounts by large companies (by location)
  Drinking Water Plants Survey (DKWP): Volumes treated, quality of intake, outflow, costs
  Survey of Industrial Processes (SIP) (pilot): processes in place to limit pollutants (adjunct to NPRI)
  No compilation of water emission accounts (report wastewater)
4. Level 2
Notes: No examples from Europe: http://ec.europa.eu/eurostat/statistics-explained/index.php/Environmental_accounts_-_establishing_the_links_between_the_environment_and_the_economy

## Slide 38: France 1990s
Basic statistics, but beginnings of an account
4. Level 2
In preparation of the 1992 water law
Shows the point polluting emissions discharged through sewerage
Natural water bodies
Households
Sewers
Industries connected to sewers
Pollution eliminated
WWTP
Examples of pollution flows in France (million tons per year)
Ministry of Environment of France, 1990s
OM=Organic Matter
TSS=Total suspended solids.
WWTP=Wastewater Treatment Plants
OM=1.105
TSS=1.745
OM=0.364
TSS=1.745
OM=0.885
TSS=1.139
OM=0.609
TSS=1.897
OM=0.583
TSS=0.885
OM=0.276
TSS=0.241
Notes: The following diagram was published in the 1990s by the Ministry of Environment of France in preparation of the 1992 water law. The diagram shows the point polluting emissions discharged through sewerage.

## Slide 39: France 1990s
Basic statistics, but beginnings of an account
4. Level 2

## Slide 40: City level: from Peal, et al., 2014
4. Level 2

## Slide 41: City level: from Peal, et al., 2014
4. Level 2

## Slide 42: Other countries?
Netherlands: Nutrients and heavy metals; based on reported emissions (kg); net approach
Source: Environment Accounts of the Netherlands 2013
4. Level 2
Measure for the environmental efficiency of production processes
=
The most intense polluter
Notes: The emission intensity is a measure for the environmental efficiency of production processes. It is equal to the total emission divided by value added.
In 2011, the emission intensity of manufacturing as a whole was equal to almost 32 equivalents per euro. In 2012 this decreased slightly to 30 equivalents per euro. Within manufacturing there are significant differences.
The biggest polluter, measured as total emission divided by value added, is manufacturing of food products, with an intensity of more than 136 equivalents per euro in 2011. Here the processing of agricultural products is responsible for the high nutrient emissions. Another big polluter is the sector manufacturing of coke and petroleum (refineries). In 2011 the emission intensity of this sector was 58 equivalents per euro. In 2012 this increased to 60 equivalents per euro. In 2011 manufacturing of food products had a share of more than 80 percent in the total emissions of phosphorus for total manufacturing. In 2012 it came to almost 76 percent. Its share in the total emissions of nitrogen was 58 percent in 2011 and almost 55 percent in 2012. Due to strict standards, the total discharge of nutrients for manufacturing was lower in 2012 than in 2011.

## Slide 43: Other countries?
Netherlands: Nutrients and heavy metals; based on reported emissions (kg); net approach
Source: Environment Accounts of the Netherlands 2013
4. Level 2

## Slide 44: Other countries
Denmark: Wastewater and monetary accounts
Others?
  Water emissions is not in EU list
    European environmental accounts: established in Regulation (EU) 691/2011
  The regulation includes…
    Air emissions accounts (AEA)
    Economy-wide material flow accounts (EW-MFA)
    Physical energy flow accounts (PEFA)
    Environmental taxes
    Environmental goods and services sector (EGSS) accounts
    Environmental protection expenditure accounts (EPEA)
  Other European environmental accounts…
    Forest accounts
    Environmental subsidies and similar transfers accounts
4. Level 2
Notes: European Environmental accounts
- The regulation provides a legal framework for a harmonized collection of comparable data from all EU member states and EFTA countries. It is consistent with the SEEA 2012 CF and structured in modules. But only some parts of the CF are presently implemented (6 modules)

## Slide 45: Take home points
Water Emission Accounts track quantities of pollutants in wastewater
  Monitor policies to reduce pollution; reduce water waste
Link to
  SEEA Water PSUT: Volume of water treated & released
  SEEA Solid Waste: Disposition of collected emissions
  SEEA EPE: Expenditures on wastewater management
  Links to FDES 3.3.2: Generation and management of wastewater
Data sources include emission factors, release reports, effluent quality monitoring
Main challenges: local factors, data from many sources
Take home points

## Slide 46: Discussion
What are the priorities?
  Which pollutants: BOD, COD, metals, nutrients, pharma?
  Which stage: generation, municipal treatment, release to environment, water reclamation?
What data are available?
Who else should be consulted?
For tomorrow:
  Look for national data for generation, treatment and release of emissions to water (nothing in CPES 2014?)
  Household, industrial factors
Discussion

## Slide 47: References
OECD PRTR (Pollutant release and transfer registry): http://www.oecd.org/chemicalsafety/pollutant-release-transfer-register/
Peal, A., Blackett, I., Hawkins, P. M. and Heymans, C. 2014. Fecal sludge management: A comparative analysis of 12 cities. Journal of Water Sanitation and Hygiene for Development, Vol. 4, No. 4, pp. 563–575. doi:10.2166/washdev.2014.026
Sato, T., Qadir, M., Yamamoto, S., Endo, T. and Zahoor, A. 2013. Global, regional, and country level need for data on wastewater generation, treatment, and use. Agricultural Water Management, Vol. 130, pp. 1–13. dx.doi.org/10.1016/j.agwat.2013.08.007
SEEA-Central Framework: http://unstats.un.org/unsd/envaccounting/seeaRev/SEEA_CF_Final_en.pdf
SEEA-Agriculture, Forestry and Fisheries: http://unstats.un.org/unsd/envaccounting/aff/2GC_Draft.pdf
UNSD. 2014. Guidelines for the Compilation of Water Accounts and Statistics (Draft). https://seea.un.org/content/water
WWAP (United Nations World Water Assessment Programme). 2017. The United Nations World Water Development Report 2017. Wastewater: The Untapped Resource. Paris, UNESCO. http://www.unesco.org/new/en/natural-sciences/environment/water/wwap/wwdr/2017-wastewater-the-untapped-resource/
References

## Slide 48: Acknowledgement
Materials prepared by:
  Michael Bordt
    Regional Advisor on Environment Statistics
    ESCAP Statistics Division bordt@un.org
    More self-learning resources on: http:/communities.unescap.org/environment-statistics
  Hye Kyeong Choi
    Consultant on Environment Statistics
    ESCAP Statistics Division gracechoi0102@gmail.com
Materials adapted from:
  Original work from SEEA-CF manual
  seea@un.org
Acknowledgement

## Slide 49: Types of water emissions and sources (1)
Group | Pollutant | Main source
Pathogens | Viruses, bacteria, helmiths | Human waste: Households, Hospitals, Hotels, …
Organic matter | Bio-degradable | Households Food industries
Nutrients | Nitrogen | Fertilizer in returns and runoff from agricultural fields Discharges from WWTPs
 | Phosphorous | Fertilizer in returns and runoff from agricultural fields; Discharges from WWTPs Detergents in sewage
Annex

## Slide 50: Types of water emissions and sources (2)
Group | Pollutant | Main source
Poisonous substances | Metals | Urban runoff Steel industry Industries using electroplating Agriculture (pesticides, herbicides, defoliants include arsenic) Industries using coal (lead) Refrigeration and air conditioning (cadmium) Leather tanning (chromium)
 | Persistent Organic Pollutants (POPs), PCBs, PBTs, ets. | Agriculture (pesticides using DDT) Electric components (PCBs for cooling) Pharma industries and households: pharmaceuticals
Other | Heat | Thermo-electric plants (cooling water)
 | Colour | Tanning, dyeing industries
 | Microbeads/plastics | Toothpaste, cosmetics, soap, textiles,…
Annex
Notes: PCB = Polychlorinated biphenyl
PBT= Persistent, bioaccumulative and toxic substances